## Slide 1: Programming Microcontrollers
A Computer Scientist’s perspective
André Pereira
March 2022

## Slide 2: Agenda
Goals & Pre-requisites
Programming abstraction levels
What’s an Instruction Set Architecture?
CISC vs RISC
Microprocessors and microcontrollers
Practical exercises

## Slide 3: Goals
Understand the architectural differences between microprocessors and microcontrollers
Learn how to code and interact with a microcontroller
Apply the fundamentals of microprocessor programming in assembly to microcontrollers

## Slide 4: Pre-requisites
Previous enrollment in the Sistemas de Computação Curricular Unit
A laptop with the AVR_SIM v2.5 tool installed
  Available for Linux and Windows
  Download: http://www.avr-asm-tutorial.net/avr_sim/index_en.html#download
  Work with a colleague!
Patience for my lack of knowledge in electronic engineering

## Slide 5: Abstraction Levels
High Level Languages (HLL)
  Independent of the hardware
  Various programming paradigms (functional, imperative, object-oriented, …)
  User usually codes at this abstraction level
    Python, C/C++, Java, …
Assembly Languages
Machine Languages

## Slide 6: Abstraction Levels
High Level Languages (HLL)
Assembly Languages
  Hardware supports a given Instruction Set Architecture (ISA)
  Availability of instructions is dependent on the hardware
  Several ISAs available
    IA-16/32, x86/x64, MIPS, …
Machine Languages

## Slide 7: Abstraction Levels
High Level Languages (HLL)
Assembly Languages
Machine Languages
  A list of commands supported by the hardware
  Dependent on the specific chip
  Chips from the same architecture may have different commands
  Represented as pure binary
  Two design philosophies, which impact the supported ISA
    Complex Instruction Set Computers (CISC)
    Reduced Instruction Set Computers (RISC)

## Slide 8: Instruction Set Architecture (ISA)
Defines a set of instructions to control the behavior of a chip
  Logic and arithmetic operations
  Operand data access
  Control of the execution flow
  Input/output and others
Imposes restrictions to the instruction representation in memory

## Slide 9: Instruction Set Architecture (ISA)
Defines a set of instructions to control the behavior of a chip
Imposes restrictions to the instruction representation in memory
  Assembly reflects the instructions at HW level
  Variable vs fixed instruction length

## Slide 10: ISA – Supported Operations
Logic and arithmetic operations
  And, or, xor, not, cmp, …
  Add, sub, mul, div, inc, dec, …
ISA defines the number of operands for each instruction
  3 operands – RISC for microprocessors (ex., ARM)
  2 operands – RISC/CISC for microprocessors (ex., IA-16)
  1 operand – RISC for microcontrollers
  0 operands – RISC/CISC

## Slide 11: ISA – Access and Types of Operands
Operand types
  Immediates
  Scalars in registers
  Complex data structures in memory (ex., C structs, arrays)
Operand data access
RISC
  L&A ops – all operands in registers
  Few address specification modes
  32 general purpose registers
CISC
  L&A ops – operands in registers or register/memory
  Several address specification modes
  8 general purpose registers (IA-16)

## Slide 12: ISA – Instruction Length in Memory
Variable instruction length
  Instructions can range from 1 to several bytes
  Representation organized in sections
    The sections used may vary between instructions
  Code requires less memory space (a big limitation in the past)
  More complex Control Units and Decoder are required
    Slow(er) fetch and decoding of a complex instruction
IA-32

## Slide 13: ISA – Instruction Length in Memory
Fixed instruction length
  Instructions often coded using 32 bits
  Representation organized in sections
    Unused sections are offset to add up to 32 bits
  Larger in-memory code bases (still a few KiBs to MeBs)
  Simpler and faster decoding
ARM

## Slide 14: Program Organization in Memory

## Slide 15: Instruction Execution on IA-16 (CISC)

## Slide 16: A CISC vs RISC Summary
CISC (IA-16)
6+2 generic registers
  Intensive use of the stack
    Local variables
    Function argument passing
    Memory accesses are not efficient!
Smaller codebases in memory
  Variable length instructions
Complex operations
  Ex. push
RISC
16 to 32 generic registers
  Stack used much less
    Fewer variables in memory
    Registers used to pass arguments to functions
    Function return address in register
Larger codebases in memory
  Fixed length instructions
Simpler operations
  Ex. push -> sub + store

## Slide 17: Microprocessor Architecture
Intel 8085 (1976)

## Slide 18: Microprocessor Architecture
Intel Ivy Bridge (2012)

## Slide 19: Microcontroller Architecture
Intel 8051 (1980)

## Slide 20: Microcontroller Architecture
Intel 8051 (1980)

## Slide 21: The Differences
Microprocessor
Chips designed for computation
  Generic operations (add, sub, …)
  Complex operations (sin, cos, …)
  Different designs for different computations
  Usually computational efficiency is key
  Fast clock speeds (up to 5.4 GHz)
  Expensive and complicated
  Must be integrated into a system
  Generic use
Microcontroller
Chips designed for electronic device control
  Integrates a simple microprocessor
  Embeds memory (volatile and non-volatile) and I/O
  Energy efficiency and thermal dissipation are key
  Slow clock speeds (< 200 MHz)
  Cheap and simple
  SoC-like
  Application specific

## Slide 22: Microcontroller Programming Models
Linear/Imperative
Program based on statements
  Change the program state
Statements define commands for the system to execute
Implements how a program performs an algorithm
Statements executed in sequence by default
C, Fortran, IA-32 ISA, …
Interrupt based
Hardware interrupts trigger function calls
  Software interrupts not usually supported
  Can happen in the middle of a multi-cycle instruction execution
Interrupts must be dealt with immediately
Functions often programmed linearly
ATMEL ISA, …

## Slide 23: Microcontroller Programming Models
Hardware interrupts trigger function calls
  Software interrupts not usually supported
  Can happen in the middle of a multi-cycle instruction execution
Interrupts must be dealt with immediately
Functions often programmed linearly
ATMEL ISA, …
Interrupt based

## Slide 24: ATMEL Microcontrollers
ATTiny13
  RISC (120 ins)
  8 bit
  32 8bit general purpose registers
  1 – 10 MHz
  1 KiBytes flash storage
  1x 8bit timer
  6 I/O lines (ports)
  …
ATMega32
  Advanced RISC Arch (131 ins)
  32 8bit general purpose registers
  32 KiBytes flash storage
  1 – 16 MHz clock
  2x 8bit + 1x 16bit timers
  32 I/O lines
Peak Instruction throughput: 1MIPS @ 1 MHz

## Slide 25: ATMEL Microcontrollers
ATTiny13
ATMega32

## Slide 26: ATTiny13
5 I/O addressable port pins: PB0 to PB4
  Each controlled by a bit in DDRB and PORTB “registers”
  DDRB (Data Direction Register port B): 1/0 -> output/input (extremely simplified, depends on breadboard setup)
  PORTB (data output register port B): 1/0 -> high/low voltage
  PINB (input register B): stores the logical state of the port pin
Processing unit programmed similarly to RISC microprocessors

## Slide 27: AVR Simulator
Tool for the simulation of code execution in microcontrollers
  Assembles the ISA to produce machine code
  Simulates ATMEL microcontrollers
Allows full control of
  View and change bits in memory and registers
  Timer and interrupt manipulation
  Microcontroller clock frequency
Looks are inversely proportional to the tool potential/usefulness

## Slide 28: Practical Session
https://github.com/ampereira90/microcontrollers

## Slide 29: A Practical Example (1)
Switch a LED on/off each couple of cycles
In a “sink” configuration, output bit turns on the LED

## Slide 30: A Practical Example (1) > led_on_off.asm file
How long does the LED stays on and off?
Let’s simulate this!

## Slide 31: A Practical Example (1) > led_on_off.asm file
Create a “New Project” in AVR_SIM
Delete all default code and implement your own
“Assemble” and then “Simulate”

## Slide 32: A Practical Example (1) > led_on_off.asm file
Create a “New Project” in AVR_SIM
Delete all default code and implement your own
“Assemble” and then “Simulate”

## Slide 33: A Practical Example (1) > led_on_off.asm file
“Step” executes the next instruction
“Run” executes the whole program

## Slide 34: A Practical Example (2) > led_on_off_stall.asm file
Let’s complicate it
  Replace the “nops” by a function call to “Stall”
  “Stall” function should delay the execution by 100 cycles

## Slide 35: A Practical Example (3) > led_on_off_counter.asm file
Implement a program that
  Reads the PINB1 bit
  If the bit is 0 add R24 to R25
  If the bit is 1 subtract R24 to R25
  Flash the LED x times with an interval of 20 cycles
    Where x is the result of the addition/subtraction
Draw a diagram of the execution flow and tasks before coding!

## Slide 36: Relevant Instructions – ATMEL ISA
IA-16 ISA | ATMEL ISA | Description
add r1, r2 | add r2, r1 | r2 = r2 + r1
sub r1, r2 | sub r2, r1 | r2 = r2 – r1
inc r1 | inc r1 | r1 = r1 + 1
dec r1 | dec r1 | r1 = r1 – 1
mov v1, r1 | ldi r1, v1 | r1 = v1
jmp label | rjmp label | ProgramCounter = label
call func | rcall func | ProgramCounter = func
jne | brne | Jump if ZF not set
- | in r1, PINB | Loads from I/O space to r1
- | out PINB, r1 | Stores r1 on I/O space
- | sbi PORTB, PORTB0 | PORTB0 bit set to 1 in PORTB
- | cbi PORTB, PORTB0 | PORTB0 bit set to 0 in PORTB
and r1, r2 | and r2, r1 | r2 = r1 & r2
and $v, r1 | andi r1, 0x00 | r1 = r1 & immediate

## Slide 37: References

## Slide 38: Programming Microcontrollers
The end
André Pereira
March 2022